## Slide 1: Noida Institute of Engineering and Technology, Greater Noida
Introduction
Faculty Name: Dr. Vivek Kumar
Affiliation: Prof.
Department: IT
Unit: 1
Subject Name
Computer Organization and Architecture
Course Details (B Tech 3rd Sem)

## Slide 2
Content
Functional units of digital system and their interconnections
Bus and types of buses
Bus arbitration
Register bus and memory transfer
Processor organization
General register organization
Stack organization
Addressing modes
*CISC (Topic Beyond Syllabus)

## Slide 3
1. Discuss the basic concepts and structure of computers
2. Understand concepts of register transfer logic and arithmetic operations
3. Explain different types of addressing modes and memory organization
4. Learn the different types of serial communication techniques
5. Summarize the Instruction execution stages
Course Objective

## Slide 4
Course Outcome
S.NO | COURSE OUTCOME(CO) | CO –DESCRIPTION
1 | KCS 302.1 | Study of the basic structure and operation of a digital computer system.
2 | KCS 302.2 | Analysis of the design of arithmetic & logic unit and understanding of the fixed point and floating-point arithmetic operations.
3 | KCS 302.3 | Implementation of control unit techniques and the concept of Pipelining
4 | KCS 302.4 | Understanding the hierarchical memory system, cache memories and virtual memory
5 | KCS 302.5 | Understanding the different ways of communicating with I/O devices and standard I/O interfaces

## Slide 5
CO-PO and PSO Mapping
 |  | COMPUTER ORGANIZATION AND ARCHITECTURE (KCS-302) |  |  |  |  |  |  |  |  |  | 
CO.K | PO1 | PO2 | PO3 | PO4 | PO5 | PO6 | PO7 | PO8 | PO9 | PO 10 | PO 11 | PO 12
KCS-302.1 | 3 | 2 | 1 | 1 | 1 | 1 | 1 | - | 1 | 1 | 1 | 2
KCS-302.2 | 2 | 2 | 2 | 2 | 1 | 1 | - | 1 | 1 | 1 | 1 | 2
KCS-302.3 | 3 | 2 | 2 | 1 | 2 | 2 | 1 | 1 | 2 | 2 | 1 | 2
KCS-302.4 | 3 | 2 | 2 | 2 | 2 | 1 | 1 | - | 1 | 1 | 1 | 2
KCS-302.5 | 2 | 2 | 2 | 1 | 2 | - | 1 | - | 1 | 2 | 2 | 2
Average | 2.6 | 2 | 1.8 | 1.4 | 1.6 | 1 | 0.8 | 0.4 | 1.2 | 1.4 | 1.2 | 2

## Slide 6
Task 1: be ensure that are you added in CAO Class Group
Task 2: Recall last topic ( Computer System and Their Interconnections) & design it on your note book.
Task 3: Explain all Parts in details as I explained to you all.
Note: Attendance will be count only those students who will do given task.
***Be honest

## Slide 7
CO-PO and PSO Mapping
 |  |  |  | COMPUTER ORGANIZATION AND ARCHITECTURE (KCS-302) |  |  |  |  |  |  |  | 
CO.K | PO1 | PO2 | PO3 | PO4 | PO5 | PO6 | PO7 | PO8 | PO9 | PO10 | PO11 | PO12
KCS-302.1 | 3 | 2 | 1 | 1 | 1 | 1 | 1 | - | 1 | 1 | 1 | 2
KCS-302.2 | 2 | 2 | 2 | 2 | 1 | 1 | - | 1 | 1 | 1 | 1 | 2
KCS-302.3 | 3 | 2 | 2 | 1 | 2 | 2 | 1 | 1 | 2 | 2 | 1 | 2
KCS-302.4 | 3 | 2 | 2 | 2 | 2 | 1 | 1 | - | 1 | 1 | 1 | 2
KCS-302.5 | 2 | 2 | 2 | 1 | 2 | - | 1 | - | 1 | 2 | 2 | 2
Average | 2.6 | 2 | 1.8 | 1.4 | 1.6 | 1 | 0.8 | 0.4 | 1.2 | 1.4 | 1.2 | 2
COMPUTER ORGANIZATION AND ARCHITECTURE (KCS-302) |  |  |  | 
CO.K | PSO1 | PSO2 | PSO3 | PSO4
KCS-302.1 | 3 | 3 | 3 | 2
KCS-302.2 | 2 | 2 | 2 | 1
KCS-302.3 | 3 | 3 | 3 | 2
KCS-302.4 | 2 | 3 | 3 | 2
KCS-302.5 | 2 | 3 | 3 | 1
Average | 2.4 | 2.8 | 2.8 | 1.6

## Slide 8
Basic knowledge of Computer Hardware
Basic knowledge of Digital Logic Design
Prerequisite and Recap

## Slide 9
A computer can be defined as a fast electronic calculating machine that accepts data, process it and produces the resulting information
List of instruction are called programs and internal storage is called computer memory
Different types of computers are
  Personal computers
  Note book computers
  Work stations
  Enterprise systems
  Super computers
Introduction

## Slide 10
A computer consist of five main parts: Input, Memory, Arithmetic logic unit (ALU), Control unit and Output
Read () : Active Low Signal (0)
Write (W) : Active High Signal (1)
IO(1)/ (0)
Functional units and their interconnections
Input
Processor
Control
ALU
Output
Memory
1001010010110000
0010100101010001
1111011101100110
1001010010110000
1001010010110000
1001010010110000
Address
Data Bus
X3=X1+X2
X1, X2 and X3 are Memory Addresses
X1: 3000
X2: 3002
X3: 3004
2000 X3=X1+X2
3000 50
3001
3002 100
3003
3004 150
RAM
/W
Instruction Details

## Slide 11
1/0
IO/
1/0
Output(1)
Input (0)
/O(1)
1/0
Write(1)
Read(0)
M(/W) 0

## Slide 12
Functional units and their interconnections (Cont.)
Input unit
  Data is transferred to a computer through input devices
  Keyboard is a most common example of input device
  Joysticks, trackballs, mouse, scanners etc are other input devices
Memory unit
  Its function is to store programs and data
  It is basically of two types: Primary and Secondary memory
  RAM and ROM are the examples of primary memory
  Magnetic disks & tapes, optical disks, floppies etc are examples of secondary memory

## Slide 13
Arithmetic logic and Shift Unit (ALU)
  Most of the computer operators are executed in ALU of the processor like addition, subtraction, division, multiplication, etc
  The operands are brought into the ALU from memory and stored in high speed storage elements called register
Timing and Control unit
  It effectively is the nerve center that sends signals to other units and senses their states
  The actual timing signals that govern the transfer of data between input unit, processor, memory and output unit are generated by the control unit
Functional units and their interconnections (Cont.)

## Slide 14
Output unit
  Its basic function is to send the processed results to the outside world
  Printer, speakers, monitor etc are the examples of output devices
Functional units and their interconnections (Cont.)

## Slide 15
Functional units and their interconnections (Cont.)
Dr. Vivek Kumar COA KCS-302 Unit I

## Slide 16
Bus
  Buses are the physical set of wires. The components of a computer systems are connected through these buses
  A data connection between two or more devices connected to the computer
  For example, a bus enables a computer processor to communicate with the memory or a video card to communicate with the memory.
  A bus is capable of being a parallel or serial bus
  There are three types of buses:
  Address bus
  Data bus
  Control bus
2. Bus and Types of Buses

## Slide 17
Address Bus
  Used to specify the address of the memory location to access
  CPU reads data or instructions from other locations by specifying the address of its location
  Each I/O device has a unique address
  CPU always outputs to the address bus and never reads from it
Data Bus
  Actual data is transferred via the data bus
  When the CPU sends an address to memory, the memory will send data via the data bus to the CPU
Bus and Types of Buses (Cont.)

## Slide 18
Control Bus
  Collection of Individual control signals
  Whether the CPU will read or write data
  CPU is accessing memory or an I/O device
  Memory or I/O device is ready to transfer data
  https://www.youtube.com/watch?v=xBYhHC8_A6o
Bus and Types of Buses (Cont.)

## Slide 19
Bus and Types of Buses (Cont.)

## Slide 20
Synchronous Bus:
Includes a clock in the control lines
A fixed protocol for communication that is relative to the clock
Advantage: involves very little logic and can run very fast
Disadvantages:
Every device on the bus must run at the same clock rate
To avoid clock skew, they cannot be long if they are fast
Asynchronous Bus:
It is not clocked
It can accommodate a wide range of devices
It can be lengthened without worrying about clock skew
It requires a handshaking protocol
Synchronous and Asynchronous Bus

## Slide 21
The arbitration procedure comes into picture whenever there are more than one processors requesting the services of bus
Because only one unit may at a time be able to transmit successfully over the bus, there is some selection mechanism is required to maintain such transfers. This mechanism is called as Bus Arbitration
Bus arbitration decides which component will use the bus among various competing requests
Various methods are available that can be roughly classified as either centralized or distributed.
3. Bus Arbitration

## Slide 22
There are three arbitration schemes
Daisy chaining
Polling
Independent requesting
Daisy chaining method
It is a centralized bus arbitration method
I n this method, all requesting components are attached serially on to the bus
This method involves three control signals
BUS REQUEST
BUS GRANT
BUS BUSY
Bus Arbitration (Cont.)

## Slide 23
All the bus units are connected to BUS REQUEST line
When activated, it indicates that one or more devices are requesting to use the bus
Bus Controller responds to a BUS REQUEST only if BUS BUSY is inactive. When bus control is given to requesting device, it enables its physical bus connection and activates BUS BUSY
W hen the first requesting device gets control of the bus and receives BUS GRANT, then it
blocks further propagation of signals, activates BUS BUSY and begins to use
When a non requesting device receives BUS GRANT signal, it forwards the signal to next device
Thus if two devices simultaneously request bus access, the device that is closer to the bus controller receives BUS GRANT and receives the bus control
The devices that are closed to the bus controller are of higher priority than those of the other devices
Bus Arbitration (Cont.)

## Slide 27
Fig: Daisy chain method
Bus Arbitration (Cont.)

## Slide 29
Bus Arbitration (Cont.)
Polling method
This method replaces the BUS GRANT line of daisy chain method with a set of poll count lines that are connected directly to all devices on the bus
Devices request access to the bus via a common BUS REQUEST line
Bus controller generates a sequence of numbers on the poll count lines
Each device compares these numbers as their device address already assigned to them
When a requesting device finds that its address matches the numbers on the poll-count lines, the device activates BUS BUSY
The bus controller responds by terminating the polling process and the device connects to the bus

## Slide 30
Fig: Polling method
Bus Arbitration (Cont.)

## Slide 31
Independent requesting method
There are separate BUS REQUEST and BUS GRANT lines for every device that are sharing bus.
In this, bus controller has the capability of immediate identifying all the requesting devices.
Bus controller responds rapidly to the request by determining the highest priority device that has sent the bus request.
This priority is programmable and is predetermined.
https://www.youtube.com/watch?v=B8_T0mMk0Ls
Bus Arbitration (Cont.)

## Slide 32
Fig: Independent Requesting Method
Bus Arbitration (Cont.)

## Slide 33
A typical digital computer has many registers, and paths must be provided to transfer information from one to another register for performing various operations in the computer system
The number of wires will be excessive if separate lines are used between each register to all other register
A more efficient and widely used method for transferring data between multiple register is common bus line system.
4.Register bus and memory transfer

## Slide 34
Common Bus System
A bus structure consist a set of common lines each for each register, through which binary information can transfer one at time.
Control signal determine that which register is connected with a bus line at time to transfer the information.
There are two ways to construct a bus
By using multiplexers.
By three state buffer.
Register bus and memory transfer (Cont.)

## Slide 35
Common bus system by using multiplexers
One way of constructing bus system is by using multiplexers. The multiplexer select the one register who’s information is transfer to another one destination register
In a bus system, multiplex K register of n bits each to produce an n lines common bus. The number of multiplexers needed to construct the bus is equal to n. Size of each mux is must be (k-1) multiplexer hence multiplexer have n data lines
Register bus and memory transfer (Cont.)

## Slide 36
For example:
For common bus system using multiplexer for 16 register each of 32 bit data transformation
Solution: In this system we require 32(number of bits) multiplexer each having size of 16-1 multiplexer(number of register) and number of selection inputs are 4
Now we will briefly discuss an example of a bus system for 4 bit data transfer
The construction of bus system for four bit, four register is shown in next slide.
Register bus and memory transfer (Cont.)

## Slide 37
Register bus and memory transfer (Cont.)

## Slide 38
Register bus and memory transfer (Cont.)
As we know that for n bit we require n multiplexer, for k register transfer we require k-1 size of multiplexer.
Here we have n=4 and k=4 hence here we use four multiplexer each having 4-1 size.
Here each register have 4 positive triggered flip- flop set. because each mux is 4-1 each multiplexer have 2 selection inputs in the bus.
we denote it by S0 and S1. This selection input select the one line output from 0 to 3 available in the each multiplexer, and applied to the output that form a bus system.
To avoid the complicated figure we just write output and input at the connection. For example output A1 of register A is connected with the input line 0 of mux(1) because that input is labeled as A1.

## Slide 39
Register bus and memory transfer (Cont.)
In this section we will discuss how registers are selected by using two using two selection inputs
The two selection lines S and S are connected to the selection inputs of all four multiplexers.
The selection lines choose the four bits of one register and transfer them into the four-line common bus.
When S1S0 =00, the 0 data inputs of all four multiplexers are selected and applied to the outputs that form the bus.
This causes the bus lines to receive the content of register A since the outputs of this register are connected to the 0 data inputs of the multiplexers.
Similarly, register B is selected if S1S0= 0 1, and so on.

## Slide 40
Table shows the register that is selected by the bus for each of the four possible binary value of the selection lines.
Register bus and memory transfer (Cont.)
Function Table for Bus
S1 | S2 | Register Selected
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D

## Slide 41
General statement representation of transferring data between registers using bus system:
The transfer of information from a bus into one of many destination registers can be accomplished by connecting the bus lines to the inputs of all destination registers and activating the load control of the particular destination register selected.
The symbolic statement for a bus transfer may mention the bus or its presence may be implied in the statement.
When the bus is includes in the statement, the register transfer is symbolized as follows.
BUS C, R1 BUS
Register bus and memory transfer (Cont.)

## Slide 42
The content of register C is placed on the bus, and the content of the bus is loaded into register R1 by activating its load control input.
If the bus is known to exist in the system, it may be convenient just to show the direct transfer.
R1 C
From this statement the designer knows which control signals must be activated to produce the transfer through the bus.
Register bus and memory transfer (Cont.)

## Slide 43
Memory Transfer
Memory Transfer The transfer of information from a memory word to the outside environment is called a read operation.
The transfer of new information to be stored into the memory is called a write operation.
A memory word will be symbolized by the letter M. The particular memory word among the many available is selected by the memory address during the transfer.
It is necessary to specify the address of M when writing memory transfer operations.
This will be done by enclosing the address in square brackets following the letter M.
Register bus and memory transfer (Cont.)

## Slide 44
Memory Read
The address register, symbolized by AR.
The data are transferred to another register, called the data register, symbolized by DR.
The read operation can be stated as follows:
Read: DR M[AR]
Register bus and memory transfer (Cont.)

## Slide 45
Memory Write
Memory write this causes a transfer of information into DR from the memory word M selected by the address in AR.
The write operation transfers the content of a data register to a memory word M selected by the address.
Assume that the input data are in register R1 and the address is in AR.
The write operation can be stated symbolically as follows
Write: M[AR] R1
Register bus and memory transfer (Cont.)

## Slide 46: 5. Processor Organization
Central Processing Unit
The CPU is made up of 3 major Components.
The CPU performs a variety of functions dictated by the type of instructions that are incorporated in the computer
In programming, memory locations are needed for storing pointers, counters, return addresses, temporary result , etc. Memory access is most time consuming operation in a computer.
It is then more convenient and more efficient to store these intermediate values in processor registers, which are connected through common bus system.

## Slide 47: Processor Organization (Cont.)
Accumulator based CPU
Initially, computers had accumulator based CPUs.
It is a simple CPU in which the accumulator contains an operand for the Instruction.
The instruction leaves the result in the accumulator.
These CPUs have zero address & single address instruction. The Advantages : Short Instruction & less memory space. Instruction cycle takes less time because it saves time in Instruction fetching due to the absence of operand fetch. The Disadvantages : Program Size increases, memory size increases. Program execution time increases due to increase in program size.

## Slide 48: Processor Organization (Cont.)
Register based CPU
Characteristics: Multiple registers are used. The use of registers result in short programs with limited instructions. The Advantages : Shorter Program size Increase in the number of registers, increases CPU efficiency. The Disadvantages : Additional memory accesses are needed. Compilers need to be more efficient in this aspect

## Slide 49: Processor Organization (Cont.)
General Register Organization
R2
R4
R1
R3
R5
R6
R7
Clock
3X8
decoder
MUX
MUX
Arithmetic logic unit
ALU
Load
(7 lines)
SELA
B bus
Output
SELD
OPR
SELB
A bus
Input
SELA SELB SELD OPR
Control word
3 3 3 5

## Slide 50: Processor Organization (Cont.)
Example of Microoperations:
R1 ←R2+R3
To Perform this operation, the control must provide binary selection variables to the following selector inputs:
1. MUX A selector (SELA): to place the content of R2 into bus A.
2. MUX B selector (SELB): to place the content of R3 into bus B.
3. ALU operation selector (OPR): to provide the arithmetic addition A+B.
Decoder destination selector (SELD): to transfer the content of the output bus into R1.
There are therefore 14 binary selection inputs , and their combination value specifies a control word.
A control Word (CW) is a word whose individual bits represent a various control signals.

## Slide 51: Processor Organization (Cont.)
Stack Organization
The stack in digital computers is essentially a memory unit with an address register (Stack Pointer SP) that count only after an initial value is loaded into the stack.
SP value always point at the top item in the stack.
The two operations of stacks are the insertion (push), and deletion (pop) of items.
A stack can be organized as a collection of a finite number of memory words or registers.
In a 64-word stack, SP contains 6 bits because 26 = 64.
The 1-bit register FULL is set to 1 when stack is full.
The 1-bit register EMTY is set to 1 when stack is empty.
DR is data register that holds the binary data to be written into or read out of the stack.

## Slide 52: Processor Organization (Cont.)
Stack Organization
B
A
C
DR
SP(Stack Pointer)
FULL
EMPTY
Address
0
1
2
3
4
63
Block diagram of
a 64 word-register stack
6 bit SP
Data
(operands)
Stack
DR (Data Register)
Computer memory with
program, data & stack segments
Program
(instructions)
Mem. Unit
Address
SP
PC (Program Counter)
AR (Address Data)
4001
4000
3999
3998
3997
3000
2000
1000
Hold data to
be w/R i/o
of stack
CPU
1504
PC-1505
PC: PC+1

## Slide 53: Processor Organization (Cont.)
In register stack
The push operation is implemented with the following sequence of microoperations:
SP SP+1 Increment stack pointer
M[SP] DR Write item on top of the stack
If (SP=0) then (FULL 1) Check if stack is full
(when 63 is incremented by 1, the result is 0.)
EMPTY 0 Mark the stack not empty
`

## Slide 54: Processor Organization (Cont.)
In register stack
The push operation is implemented with the following sequence of microoperations:
SP SP+1 Increment stack pointer
M[SP] DR Write item on top of the stack
If (SP=0) then (FULL 1) Check if stack is full
(when 63 is incremented by 1, the result is 0.)
EMPTY 0 Mark the stack not empty

## Slide 55: Processor Organization (Cont.)
In register stack
The pop operation consists the following sequence of microoperations:
DR M[SP] Read item from top of the stack
SP SP-1 Decrement stack pointer
If (SP=0) then (EMPTY 1 ) Check if stack is empty
FULL 0 Mark the stack not full
A stack can exist as a stand-alone unit or can be implemented in a RAM attached to a CPU.

## Slide 56: Processor Organization (Cont.)
In memory stack
A stack can be implemented in a portion of a random –access memory attached to a CPU, and using a processor register as SP as shown the diagram above.
In the diagram shown Computer memory with program, data & stack segments:
PC (points at the address of the next instruction) is used during the fetch phase to read an instruction.
AR (points at an array of data) is used during the execution phase to read an operand.
SP is used push or pop items into or from the stack
The three registers are connected to a common address bus, & either one can provide an address for memory.
Push: insert (write) new item at the top of the stack
SP ← SP – 1, M[SP] ← DR
Pop: delete (read) the top item from the stack
DR ← M[SP], SP ← SP + 1

## Slide 57: Processor Organization (Cont.)
In memory stack
The stack limits (overflow) can be checked by using 2 processor registers:
One to hold the upper limit (3000 in this example)
Another to hold the lower limit (4001 in this example )
SP is compared with the upper limit register after each push operation.
SP is compared with the lower limit register after each pop operation.
How many microoperations are needed then for the pop or push operations?
Two microoperations are needed for push or pop :
1. An access to memory through SP
2. Updating SP

## Slide 58: Processor Organization (Cont.)
Reverse Polish Notation
A stack organization is very effective for evaluating arithmetic expressions.
The reverse Polish notation is in a form suitable for stack manipulation, where the infix expression A*B+C*D can be written in Reverse Polish Notation (RPN or postfix notation) as: AB*CD*+
Example: Stack operation to evaluate 3*4+5*6
=> 34*56*+ (in in reverse Polish notation )
3
3
3
4
4
12
*
12
5
5
12
6
5
6
12
30
*
42
+

## Slide 61
(4*2)+(5-2)+((6+4)*(1+1))

## Slide 62
(i) (A*B)+(C*D)+(E*F)
Prefix (*AB)+(*CD)+(*EF)= (+*AB*CD)+(*EF)=++*AB*CD*EF
Postfix (AB*)+(CD*)+(EF*)=(AB*CD*+EF*+)
(ii) (A*B)+A*((B*D)+(C*E))
(*AB)+A*((*BD)+(*CE))
(*AB)+A*(+*BD*CE)
(*AB)+(*A+*BD*CE)
+*AB*A+*BD*CE
(iii) A*[B+(C*D)+E]/F*(G+H)
A*[B+(CD*)+E]/F*(GH+)
A*[(BCD*+)+E]/(FGH+*)
(ABCD*+E+*)/ (FGH+*)
ABCD*+E+*FGH+*/
A*B+(C*D)+E/F*(G+H)

## Slide 63: Processor Organization (Cont.)
Instruction Formats
The bits of the instruction are divided into groups called fields.
The most common fields founded in the instruction formats are:
1. An operation code field
2. An address field
3. A mode field
Data executed by instructions (operands) are stored either in memory or in processor registers.
Operands residing in memory are specified by their memory address.
Operands residing in registers are specified with a register address.

## Slide 64: Processor Organization (Cont.)
Instruction Formats
A register address is binary number of k bits that defines one of 2^k registers in the CPU.
Most computers fall into one of the 3 types of CPU organizations:
1. Single Accumulator (AC) Organization, i.e. ADD X
2. General register (Rs) Organization, ADD R1,R2,R3
3. Stack Organization, i.e. ADD (pop and add 2 operand then push the result into the stack)
Some computers combine features from more than one organization structure, Ex. Intel 8080 (GRs for register transfer, AC used in arithmetic operations)

## Slide 65: Processor Organization (Cont.)
Addressing modes
The addressing mode specifies a rule for interpreting or modifying the address field of the instruction before the operand is actually executed.
Computers use addressing mode techniques for the purpose of accommodating one of the following provisions:
1. To give programming versatilities to the user to be more flexible.
2. To reduce the number of bits in the addressing field of the instruction.
In some some computers, the addressing mode of the instruction is specified with distinct binary code.
Instruction format with mode field
Address
Mode
Opcode

## Slide 66: Processor Organization (Cont.)
Addressing modes
Other computers use a single binary for operation & Address mode.
The mode field is used to locate the operand.
Address field may designate a memory address or a processor register.
There are 2 modes that need no address field at all (Implied & immediate modes).
The most well known addressing mode are:
Implied mode.
Immediate mode
Register mode
Register Indirect mode
Auto-increment or Auto-decrement mode
Direct Mode
Indirect Mode
Relative Address Mode
Index Addressing Mode

## Slide 67
Add C [AC]=[AC]+[C] AC(Accumulator)
LDA(Load Accumulator) 30
  R1
Add B, D B=B+D
AND R4, R2, R3 R4=R2^R3
Add
Sub
80
50
7
3
34

## Slide 68: SUB 45 [AC]=[AC]-45 ADD B, 3000 [B]=[B]+M[3000] ADD B, 3000, 3002 B=M[3000]+M[3002] ADD 3000, 3002 M[3000]=M[3000]+M[3002] ADD B,M
Hex Programming
Hexadecimal
0-9, A-F
Registers : B-C, D-E, H-L(8-8 Bits)
4-bits (address): 6754/ AB45
2-bits: (data) : 56/A9/8F
ADD B,45 B=B+45

## Slide 69
1.Register Addressing
ADD B, C B=B+C
SUB D,H, L D=H-L
2. Direct Addressing At least one operand will be RAM address
ADD 2000, 3000
M[2000]= M[2000]+M[3000]
SUB 3000, B, 2000
M[3000]=[B]-M[2000]
ADD 3000 [AC]=[AC]+M[3000]
3. Indirect Addressing
ADD B,C, M effective address = 3000
[B]=[C]+M[[H-L]]
[B]=[B]+M[3000] [B]=20+70
B: 20 | C:30
D: | E:
H: 30 | L:00
ALU
AC: 50
Address | Data
2000 | 50
2001 | 
2002 | 
……. | 
3000 | 70
3001 | 
3002 | 
….. | 
RAM(Main Memory)
4. Immediate Addressing | at least one operand will be data
ADI B, 30H | ADI C, 60
[B]=[B]+30 | 
SUI 50 | [AC]=[AC]-50

## Slide 70
Relative Addressing Mode:
Effective address= [PC]+address part of instruction
Index Addressing Mode
Effective address= [index register]+address part of instruction
Base Addressing Mode
Effective Address = [Base Register]+address part of instruction
Implied Mode: without operands
work on content of AC only 10101=01010
Comp/ INC
Or on stack
ADD
/SUB
: it will work on Stack only
 | 70
 | 50
 | 60

## Slide 73: Processor Organization (Cont.)
Numerical Example
Address=500
Next Instruction
450
700
800
900
325
300
Load to AC Mode
Memory
500
Address
201
202
399
400
702
600
200
800
PC=200
R1=400
XR=100
AC
Addressing mode eff. Add Content of AC
-----------------------------------------------------------
Direct Address 500 800
Immediate operand 201 500
Indirect Address 800 300
Relative Address 702 (PC=PC+2) 325
Indexes Address 600 (XR+500) 900
Register --- 400
Register Indirect 400 700
Auto-increment 400 700
Auto-decrement 399 450
Tabular list

## Slide 74: Processor Organization (Cont.)
Different ways in which the address of an operand in specified in an instruction is referred to as addressing modes.
Register mode
  Operand is the contents of a processor register.
  Address of the register is given in the instruction.
  E.g. Clear R1
Absolute mode
  Operand is in a memory location.
  Address of the memory location is given explicitly in the instruction.
  E.g. Clear A
  Also called as “Direct mode” in some assembly languages
Register and absolute modes can be used to represent variables

## Slide 75: Processor Organization (Cont.)
Immediate mode
  Operand is given explicitly in the instruction.
  E.g. Move #200, R0
  Can be used to represent constants.
Register, Absolute and Immediate modes contained either the address of the operand or the operand itself.
Some instructions provide information from which the memory address of the operand can be determined
  That is, they provide the “Effective Address” of the operand.
  They do not provide the operand or the address of the operand explicitly.
Different ways in which “Effective Address” of the operand can be generated.

## Slide 76: Processor Organization (Cont.)
Indirect Mode
Effective Address of the operand is the contents of a register or a memory location whose address appears in the instruction
R1
Add (R1),R0
Add (A),R0
Register
B
B
Operand
memory
Main
A
B
Operand
B
Register R1 contains Address B
Address B has the operand
Address A contains Address B
Address B has the operand
R1 and A are called “pointers”

## Slide 77: Processor Organization (Cont.)
Indexing Mode
Effective Address of the operand is generated by adding a constant value to the contents of the register
R1
Add 20(R1),R0
1000
1020
offset = 20
1000
Operand
Operand is at address 1020
Register R1 contains 1000
Offset 20 is added to the
contents of R1 to generate the
address 20
Contents of R1 do not change in the
process of generating the address
R1 is called as an “index register”
What address would be generated
by Add 1000(R1), R0 if R1 had 20?

## Slide 78: Processor Organization (Cont.)
Relative mode
Effective Address of the operand is generated by adding a constant value to the contents of the Program Counter (PC).
Variation of the Indexing Mode, where the index register is the PC
instead of a general purpose register.
When the instruction is being executed, the PC holds the address of the next instruction in the program.
Useful for specifying target addresses in branch instructions.
Addressed location is “relative” to the PC, this is called “Relative Mode”

## Slide 79: Processor Organization (Cont.)
Autoincrement mode
  Effective address of the operand is the contents of a register specified in the instruction.
  After accessing the operand, the contents of this register are automatically incremented to point to the next consecutive memory location.
  (R1)+
Autodecrement mode
  Effective address of the operand is the contents of a register specified in the instruction.
  Before accessing the operand, the contents of this register are automatically decremented to point to the previous consecutive memory location.
  -(R1)
Autoincrement and Autodecrement modes are useful for implementing “Last-In-First-Out” data structures

## Slide 80: Video Links
Youtube videos links:
https://www.youtube.com/watch?v=xBYhHC8_A6o
https://www.youtube.com/watch?v=B8_T0mMk0Ls
https://www.youtube.com/watch?v=Za7ozdjE8VI
https://www.youtube.com/watch?v=u-sp4gBAJKI

## Slide 81: Daily Quiz
1. RTL stands for:
  a. Random transfer language
  b. Register transfer language
  c. Arithmetic transfer language
  d. All of these
  2. The register that includes the address of the memory unit is termed as the :
a. MAR
b. PC
c. IR
d. None of these
3. Which are the operation that a computer performs on data that put in register:
a. Register transfer
b. Arithmetic
c. Logical
d. All of these

## Slide 82: Daily Quiz
4. Which operation puts memory address in memory address register and data in DR:
a. Memory read
b. Memory write
c. Both
d. None
5. A stack organized computer uses instruction of
  a. Indirect addressing
  b. Two addressing
  c. Zero addressing
  d. Index addressing
  6. A flip flop is a binary cell capable of storing information of
a. One bit
b. One byte
c. Zero bit
d. Eight bits

## Slide 83: Daily Quiz
7. To resolve the clash over the access of the system BUS we use ______ a. Multiple BUS b. BUS arbitrator c. Priority access d. None of the mentioned
8. The device which is allowed to initiate data transfers on the BUS at any time is called _____ a. BUS master b. Processor c. BUS arbitrator d. Controller

## Slide 84: Weekly Assignments
1. Explain various methods of bus arbitration. [CO1]
2. Discuss various types of processor organization. [CO1]
3. Explain different addressing modes with the help of diagrams. [CO1]
4. Give the structure of a basic sequential ALU. [CO1]
5. Discuss the concept of register transfer. [CO1]
6. Explain different types of addressing modes. [CO1]
7. Differentiate between Computer Organization and Computer Architecture. [CO1]
8. Explain the concept of General Register Organization in detail. [CO1]

## Slide 85: MCQ
1. To resolve the clash over the access of the system BUS we use ______ a) Multiple BUS b) BUS arbitrator c) Priority access d) None of the mentioned
Answer: b
2. The device which is allowed to initiate data transfers on the BUS at any time is called _____ a) BUS master b) Processor c) BUS arbitrator d) Controller Answer: a
3. ______ BUS arbitration approach uses the involvement of the processor. a) Centralized arbitration b) Distributed arbitration c) Random arbitration d) All of the mentioned Answer: a

## Slide 86: MCQ
4. The circuit used for the request line is a _________ a) Open-collector b) EX-OR circuit c) Open-drain d) Nand circuit Answer: c
5. The Centralized BUS arbitration is similar to ______ interrupt circuit. a) Priority b) Parallel c) Single d) Daisy chain Answer: d
6. When the processor receives the request from a device, it responds by sending _____ a) Acknowledge signal b) BUS grant signal c) Response signal d) None of the mentioned Answer: b

## Slide 87: MCQ
7. In Centralized Arbitration ______ is/are is the BUS master. a) Processor b) DMA controller c) Device d) Both Processor and DMA controller Answer: d
8. Once the BUS is granted to a device ___________ a) It activates the BUS busy line b) Performs the required operation c) Raises an interrupt d) All of the mentioned Answer: a
9. The BUS busy line is made of ________ a) Open-drain circuit b) Open-collector circuit c) EX-Or circuit d) Nor circuit Answer: b

## Slide 88: MCQ
10. After the device completes its operation _____ assumes the control of the BUS. a) Another device b) Processor c) Controller d) None of the mentioned Answer: b
11. The BUS busy line is used __________ a) To indicate the processor is busy b) To indicate that the BUS master is busy c) To indicate the BUS is already allocated d) None of the mentioned Answer: c
12. Distributed arbitration makes use of ______ a) BUS master b) Processor c) Arbitrator d) 4-bit ID Answer: d

## Slide 89: MCQ
13. In Distributed arbitration, the device requesting the BUS ______ a) Asserts the Start arbitration signal b) Sends an interrupt signal c) Sends an acknowledge signal d) None of the mentioned Answer: a
14. How is a device selected in Distributed arbitration? a) By NANDing the signals passed on all the 4 lines b) By ANDing the signals passed on all the 4 lines c) By ORing the signals passed on all the 4 lines d) None of the mentioned Answer: c
15. If two devices A and B contesting for the BUS have ID’s 5 and 6 respectively, which device gets the BUS based on the Distributed arbitration. a) Device A b) Device B c) Insufficient information d) None of the mentioned Answer: b

## Slide 90: MCQ
16. The decoded instruction is stored in ______ a) IR b) PC c) Registers d) MDR Answer: a
17. The instruction -> Add LOCA, R0 does _______ a) Adds the value of LOCA to R0 and stores in the temp register b) Adds the value of R0 to the address of LOCA c) Adds the values of both LOCA and R0 and stores it in R0 d) Adds the value of LOCA with a value in accumulator and stores it in R0 Answer: c
18. Which registers can interact with the secondary storage? a) MAR b) PC c) IR d) R0 Answer: a

## Slide 91: MCQ
19. During the execution of a program which gets initialized first? a) MDR b) IR c) PC d) MAR Answer: c
20. Which of the register/s of the processor is/are connected to Memory Bus? a) PC b) MAR c) IR d) Both PC and MAR Answer: b
21. ISP stands for _________ a) Instruction Set Processor b) Information Standard Processing c) Interchange Standard Protocol d) Interrupt Service Procedure Answer: a

## Slide 92: MCQ
22. The internal components of the processor are connected by _______ a) Processor intra-connectivity circuitry b) Processor bus c) Memory bus d) Rambus Answer: b
23. ______ is used to choose between incrementing the PC or performing ALU operations. a) Conditional codes b) Multiplexer c) Control unit d) None of the mentioned Answer: b
24.The registers, ALU and the interconnection between them are collectively called as _____ a) process route b) information trail c) information path d) data path Answer: d

## Slide 93: MCQ
25. In the case of, Zero-address instruction method the operands are stored in _____ a) Registers b) Accumulators c) Push down stack d) Cache Answer: c
26. The addressing mode which makes use of in-direction pointers is ______ a) Indirect addressing mode b) Index addressing mode c) Relative addressing mode d) Offset addressing mode Answer: a
27. The addressing mode/s, which uses the PC instead of a general purpose register is ______ a) Indexed with offset b) Relative c) Direct d) Both Indexed with offset and direct Answer: b

## Slide 94: MCQ
28. The addressing mode, where you directly specify the operand value is _______ a) Immediate b) Direct c) Definite d) Relative Answer: a
29. _____ addressing mode is most suitable to change the normal sequence of execution of instructions. a) Relative b) Indirect c) Index with Offset d) Immediate Answer: a
30. The small extremely fast, RAM’s are called as _______ a) Cache b) Heaps c) Accumulators d) Stacks Answer: a

## Slide 95: MCQ
31. The ALU makes use of _______ to store the intermediate results. a) Accumulators b) Registers c) Heap d) Stack Answer: a
32. The control unit controls other units by generating ___________ a) Control signals b) Timing signals c) Transfer signals d) Command Signals Answer: b
33. ______ are numbers and encoded characters, generally used as operands. a) Input b) Data c) Information d) Stored Values
Answer: b

## Slide 96: MCQ
34. To reduce the memory access time we generally make use of ______ a) Heaps b) Higher capacity RAM’s c) SDRAM’s d) Cache’s Answer: d
35. ______ is generally used to increase the apparent size of physical memory. a) Secondary memory b) Virtual memory c) Hard-disk d) Disks Answer: b

## Slide 97: Old University Question Papers

## Slide 98: Expected Question for Exams
Describe Sequential Arithmetic & Logic unit (ALU) using proper diagram
A digital computer has a common bus system for 16 registers of 32 bits each. The bus is constructed with multiplexers. (i) How many selection inputs are there in each multiplier? (ii) What sizes of multiplexers are needed? (iii) How many multiplexers are there in the bus?
Explain different addressing modes.
Explain the importance of different addressing modes in computer architecture with suitable example.
What is an instruction format? Explain different types of instruction formats in detail.
A digital computer has a common bus system for 16 register of 32 bits each. The bus is Constructed with multiplexers.
(i) How many selection inputs are there in each multiplexer?
(ii) What sizes of multiplexers are needed?
(iii) How many multiplexers are there in the bus?

## Slide 99: Expected Question for Exams
What is the difference between a direct and indirect address instruction? How many references to memory are needed for each type of instruction to bring an operand into a processor register?
A computer has 16 register, an ALU with 32 operations and a shifter with eight operations all Connected to a common bus system.
(i) Formulate a control word for a micro operation.
(ii) Specify the number of pits in each field on the control word and give a general encoding scheme.
Convert the following arithmetic expressions from infix to reverse polish notation:-
(i) A*B+C*D+E*F
(ii) A*B+A*(B*D+C*E)
(iii) A*[B+C*CD+E]/F*(G+H)

## Slide 100: Expected Questions for Exams
Explain tri state buffer with their application.
How many types of address sequence are required in a control memory? Explain with the diagram of a control memory and it’s associated hardware.
Explain architecture of computer system.
Explain daisy chain priority.
Discuss the concept of bus arbitration.
Discuss stack organization. Explain the following in detail:
i) Register stack
ii) Memory stack

## Slide 101: Summary
A computer system consists of software and hardware. Software, or program enables a computer to perform specific tasks, as opposed to the physical components of the system (hardware).
Computer hardware is the physical part of a computer, including the digital circuitry, as distinguished from the computer software that executes within the hardware.
Computer architecture is defined as the science and art of selecting and interconnecting hardware components to create computers that meet functional, performance and cost goals.
A computer architecture is considered as a series of abstraction layers: hardware, firmware, assembler, kernel, operating system and applications
A program has a sequence of instructions which gets executed through a cycle , called instruction cycle. The basic parts of and instruction cycle include fetch, decode, read the effective address from memory and execute.

## Slide 102: References
Computer Organization & Architecture: Designing for Performance, Stalling, PHI.
Computer Organization and Architecture, Stalling, Pearson Education.
Computer System Architecture, Morris Mano, PHI.
https://www.youtube.com/watch?v=xBYhHC8_A6o
https://www.youtube.com/watch?v=B8_T0mMk0Ls
https://www.youtube.com/watch?v=Za7ozdjE8VI
https://www.youtube.com/watch?v=u-sp4gBAJKI